## Slide 1: Optimizing Doppler Imaging
Beyond Black and White

## Slide 2: Is Color Doppler Angle Corrected ?
No! Color Doppler is steered
Color Doppler uses thousands of sample volumes to analyze millions of blood cells.
All blood cells are moving in random directions at unknown angles.
Throw in some Rayleigh scattering and it is impossible to detect and correct for all angles of blood cell movement.

## Slide 3
Flow
Color Doppler Steering
Typically steer 20 degrees left/right of center.
Color displays will change as angle of insonation changes.
Center steer on a 90-degree vessel will show colors from both flow directions.

## Slide 4: Angle of Insonation
A color display is totally dependent on the angle of insonation.
Flows acquired at angles close to 0 degrees will have a “brighter” appearance than identical flows acquired at angles closer to 60 degrees.
Do not confuse clinically significant aliased flow with angle created aliasing.

## Slide 5
Angle of Insonation
Flows detected at angles closer to 0 degrees will be brighter than
flows detected closer to 60 degrees.
0 degrees
90 degrees
This angle results in a dimmer color
This angle results in a brighter color
FLOW

## Slide 6: Color Steering (slant scan)
Controls the position and angle of the color window.
Aids in achieving the optimal angle of insonation for maximum color sensitivity, color rendition and artifact reduction.
Flow

## Slide 7
Why is there no color?
Steering, 90 degrees

## Slide 8
Steering- creates an angle < 90 degrees

## Slide 9
Why is there no color?
Steering effects incident angle. Steering incorrectly created a 90-degree angle

## Slide 12: Steering
When we have a rectangular image:
  we adjust the size of the box
  AND we must steer the box
  Steering the box allows us to obtain the optimal Doppler angle on a vessel

## Slide 13: How to Steer
Steering is relatively easy once you get used to how it should look. There are several ways you can remember how to steer:
  The part of the vessel headed “uphill” should be heading toward the sharp upper corner of the color box.
  The most anterior portion of the vessel should match the leading edge of your color box. The leading edge is the portion that won’t intersect your color box if you draw a straight line down.
  If your image is transverse on the vessel, you should set your color box to match the image (square or rectangle)
The color box

## Slide 15: Transverse vessels = straight color box

## Slide 16: Steering Correctly

## Slide 17: Steering Correctly

## Slide 18
Steering and PW

## Slide 19: Color Gain
Amplifies the overall strength of the returning color freq. shifts.
Does not increase insonation power.
Allows control of the amount of color in a vessel.
Always > color gain until color splash occurs then < to appropriate level.

## Slide 22
Which control was adjusted?
Color gain decreased

## Slide 23: Color Scale (PRF)
Know your anatomy and the normal flow velocity of the vessel
Think of the Color Scale as the speed limit.
  High velocity vessels have a higher speed limit so a higher color scale
    Larger arteries, main arteries
  Lower velocity vessels have a slower speed limit so a lower color scale
    Veins, smaller arteries within organs, vertebral arteries
Scale will automatically adjust other controls i.e.. frame rate, acoustic output and wall filters.
Not all ultrasound equipment have the same settings for Color and Doppler

## Slide 25: Aliasing
As in spectral Doppler the color signals will “Alias” if the speed of the blood exceeds 1/2 of the PRF/scale.
Red will wrap into blue or just the opposite depending on the direction of flow.
Color uses lower PRF/scale numbers so aliasing is more prevalent than in spectral Doppler.

## Slide 27: What about flow reversal?
Flow reversal is always easy to determine by the color display.
The primary directional colors displayed in the map you have chosen will always be separated by black,(the baseline color).

## Slide 29: How do you correct color aliasing?
Increase the scale which is increase PRF
Appears as if there is bi-directional flow

## Slide 32: Is Turbulence Displayed the Same Way as Aliasing?
NO !!! A turbulent display will be made up of a mosaic of multi-directional signals (colors).
A turbulent display will separate the primary colors, (red/blue) with the baseline color (black) and a mixture of other colors.
An aliased display will separate the primary colors with other colors depending on the color map but never with black.

## Slide 33: What Does Mosaic Pattern Mean ?
A mosaic pattern is simply a mixture of all the available color map colors distributed in random patterns as turbulent freq. shifts would be.
Turbulent blood flow would have blood cells moving in all directions (even reverse) and a mosaic pattern is a display of this activity.

## Slide 34: QUIZ QUESTION
Which image represents turbulence?
What is it called when the Doppler spectrum fills in?
A
B

## Slide 35: Wall filter

## Slide 39: Color Doppler Penetration
CDI penetration can be increased by lowering the Doppler transmit freq..
Lower X-mit freq. > penetration but < signal size so low/slow flow signals may be lost.
Higher X-mit freq. < penetration but > signal size so low/slow flow signals may be gained.

## Slide 40
Which control was adjusted?
Color gain decreased

## Slide 41
What artifact is demonstrated?
What was adjusted to correct the image?
Aliasing
Scale:PRF

## Slide 42
No color in image 1. What was done to get the color in image 2?
Color Gain- increased