## Slide 1: Intensities
Chapter 5

## Slide 2: Intensities
If you were asked to measure an ultrasound beam’s intensity, where would you measure it?
How would you report it?

## Slide 3: The 5 key words for intensities
Peak
  maximum value
Average
  mean / middle value
Spatial
  referring to location (distance) or space

## Slide 4: The 5 key words for intensities
Pulsed
  referring to the transmit time only
  Pulse is the average intensity for the pulse duration only
Temporal
  referring to all time (transmit and receive)
  A pulsed ultrasound beam does not have the same intensity at different times because sometimes it is pulsing and sometimes it is not!

## Slide 5: Intensities
Note the intensity varies:
depth time
          width

## Slide 6: Spatial Considerations
Peak
Average
Notes: The beam hitting the wall at any given distance will have areas of bright spots and areas of shadow

## Slide 7: Spatial Considerations
Two possible methods can be used:
Spatial Peak Intensity or Isp
  referring to the location of maximum intensity within the beam
2. Spatial Average Intensity or Isa
  average intensity in the cross- sectional area of the beam

## Slide 8: Temporal Considerations
Temporal refers to time
With ultrasound beams that are pulsed their intensity will change over time

## Slide 9: Temporal Considerations
Temporal Peak Intensity Itp
  measures the beam’s intensity at the moment it has reached its maximal value
2. Imax or Im
measurement of the average intensity of the most intense half cycle in the pulse
½ cycle
Notes: These are 2 ways of measuring the “peak” intensity at a point in time

## Slide 10: Temporal Considerations
3. Pulse Average Intensity Ipa
  is the average intensity of the pulse duration (transmit)
4. Temporal Average Intensity Ita
  is derived from the average intensity of the PRP (the transmit and receive time).
    *This is the lowest value because it includes off time / no beam intensity
Transmit
time only

## Slide 11: Temporal Considerations
1st The highest intensity is Itp
2nd Imax or Im
3rd Pulse Average Intensity Ipa
Lowest is Ita
    it includes not only the pulse time but also the listening time it can be up to 500 times lower than the other three

## Slide 12: Combining Spatial & Temporal Factors
When studying bioeffects of the ultrasound beam the intensity MUST be described accurately with respect to time and space
In order to do this the preceding factors are combined to form one unit
Isptp Isppa, Ispta and Isata

## Slide 13: 6 Methods to Measure and Report Intensity (units W/cm2)
SPTP | Spatial peak, temporal peak
SATP | Spatial average, temporal peak
SPTA | Spatial peak, temporal average
SATA | Spatial average, temporal average
SPPA | Spatial peak, pulse average
SAPA | Spatial average, pulse average

## Slide 14: 10 Commandments of Intensity
Intensities may be reported in various ways with respect to time and space.
The different measurements of intensities are important in the study of Bioeffects.
  SPTA intensity is most relevant with respect to tissue heating.
All intensities have units of watts/cm2
Because peak measurements are larger than average measurements, SPTP intensity has the highest value and SATA has the lowest value. (peaks are higher than averages!)

## Slide 15
5. A number called the beam uniformity coefficient (also called SP/SA factor) describes the spread of the beam in space. This coefficient is unit-less and has a value of 1 or greater.
6. The duty factor describes the relationship of beam intensities with time. The duty factor is unitless and has a value between 0 and 1.
7. For continuous wave ultrasound, the beam is always “on” and the pulse average and temporal average intensities are the same.
So: SPTA = SPPA and SATA= SAPA
10 Commandments of Intensity

## Slide 16
Continuous wave beams have a higher average than pulsed wave beams
8.
When pulsed and continuous wave sound beams have the same SPTP intensities, the continuous wave beam has the higher SPTA intensity.
When pulsed and continuous wave sound beams have the same SATP intensity, the continuous wave beam has the higher SATA intensity.
10 Commandments of Intensity
Notes: When Peaks are the same, CW has the higher Average

## Slide 17
9. Temporal considerations
  Temporal peak intensity is the (Itp) maximum in time.
  Maximum intensity (Im) is averaged over the most intense half-cycle
  Pulse average intensity (Ipa) is averaged only during the pulse duration
  Temporal average intensity (Ita) is averaged during the PRP (on and off time)
10. Spatial Considerations
  Spatial peak intensity is the maximum in space
  Spatial average intensity is averaged over the cross sectional area of the beam.
10 Commandments of Intensity

## Slide 18: Rank Intensities
1 | SPTP | Spatial peak, temporal peak
 | SATP | Spatial average, temporal peak
3 | SPTA | Spatial peak, temporal average Why is this one important?
4 | SATA | Spatial average, temporal average
2 | SPPA | Spatial peak, pulse average
 | SAPA | Spatial average, pulse average
Notes: Most relevant for bioeffects/tissue heating