## Slide 1: The Range Equation
Chapter 7

## Slide 2: Remember…
To create images, our machine emits a sound pulse that travels to a reflector located in the body then returns to the transducer.

## Slide 3: Time-of-Flight
The time that passes between the pulse creation and the pulse reception is called the go-return time or time-of-flight

## Slide 4: Superficial Reflectors
Superficial reflectors have a short time-of-flight because the time it takes for the pulse to leave the transducer and return to the transducer is short.
Superficial reflector

## Slide 5: Deep Reflectors
Deep reflectors - have a longer time-of-flight because the time it takes for the pulse to leave the transducer and return to the transducer is longer.
Deep reflector

## Slide 6: Time-of-Flight
Directly related to depth
  Deeper depth – longer time-of-flight
  Shallow depth – shorter time-of-flight
If depth is doubled, time of flight is doubled
If depth is halved, time of flight is halved

## Slide 7: Our Ultrasound System
Ultrasound systems determine reflector depth by measuring the time that it takes for the pulse to return to the transducer.
They are programmed with the average speed of sound being 1540 m/s.
By calculating how deep a reflector is, our machine can place it at the proper depth in the image

## Slide 8: Speed of Sound = depth x time
Example:
  A sound wave is created by a transducer, reflects off of an object and returns to the transducer. The depth of the reflector is 10 cm. The round-trip time is 2 seconds. What is the speed of sound in the medium?
  The sound traveled to the reflector and back, so it traveled a total of 10 cm to the reflector and 10 cm back to the transducer.
  The sound travels 20 cm in 2 seconds.
  20/2 = 10 cm/sec
  Speed of sound in the medium = 10 cm/sec
Notes: Page 54 question

## Slide 9: Calculating the Reflector Depth
Depth of reflector (mm) =
propagation speed (mm/ms) x go-return time (ms)
2
Or SOFT TISSUE
depth (mm)=1.54 mm/ms x go-return time (ms)
2

## Slide 10: The 13-Microsecond Rule
In soft tissue only!!!
For every 13 ms of go-return time, the object creating the reflection is 1 cm deep in the body
So…
  When a reflector is 2 cm deep, the go-return time is 26 ms.
  When a reflector is 3 cm deep, the go-return time is 39 ms

## Slide 11: IMPORTANT
Since a pulse travels to the reflector and back to the transducer, the total distance that a pulse travels is twice the reflector depth.

## Slide 12: Example #1
In soft tissue, how deep is a reflector in the body if the time-of-flight is 26 microseconds?
Remember the 13-microsecond rule!!!
  26/13 = 2
  2 cm deep

## Slide 13: Example #2
In soft tissue, How deep is a reflector if the time-of-flight is 130 ms?
  130/13= 10
  10 cm deep

## Slide 14: PRP
When a sonographer adjusts a systems maximum imaging depth, the PRP is altered.
Because PRP is the time from the start of one pulse to the start of another pulse, it is the same thing as the GO-RETURN TIME, or the time of flight!!!
In soft tissue:
PRP (ms) = imaging depth (cm) x 13 (ms/cm)

## Slide 15
REVIEW: Pulse duration (transmit time) cannot be changed by the sonographer (fixed by transducer).
Note: what is changed is the listening time.
a. When DOV is shallow, PRP is short
b. When the DOV is deep, the PRP is long
Listening time
Listening time

## Slide 16: A sonographer increases the imaging depth from 40mm to 180mm. What is the PRP of the new depth?
Mathematically, in soft tissue:
PRP (µs) = imaging depth (cm) x 13 (µs/cm)
PRP (µs) = 18 (cm) x 13 (µs/cm)
PRP (µs) = 18 x 13 (µs)
PRP (µs) = 234 (µs)

## Slide 17: The initial depth utilized to image the thyroid is 5cm. What is the PRP for this imaging depth?
PRP (µs) = imaging depth (cm) x 13 (µs/cm)
PRP (µs) = 5 (cm) x 13 (µs/cm)
PRP (µs) = 5 x 13 (µs)
PRP (µs) = 65 (µs)

## Slide 18: What is the PRP of an object located at a depth of 190mm, assuming you are using a 3.5MHz transducer?
PRP (µs) = imaging depth (cm) x 13 (µs/cm)
PRP (µs) = 19 (cm) x 13 (µs/cm)
PRP (µs) = 19 x 13 (µs)
PRP (µs) = 247 (µs)

## Slide 19: A sonographer alters his DOV from 220mm to 15cm. What is the PRP of the original depth?
PRP (µs) = imaging depth (cm) x 13 (µs/cm)
PRP (µs) = 22 (cm) x 13 (µs/cm)
PRP (µs) = 22 x 13 (µs)
PRP (µs) = 286 (µs)
Be SURE to READ THE QUESTION!

## Slide 20: The sonographer decided to alter the depth to better visualize a structure located in the near field. The new depth is 30mm. What is the PRP for this new depth?
PRP (µs) = imaging depth (cm) x 13 (µs/cm)
PRP (µs) = 3 (cm) x 13 (µs/cm)
PRP (µs) = 3 x 13 (µs)
PRP (µs) = 39 (µs)

## Slide 21
From our calculations what happens to the PRP as you increase depth?
39 µs | 3 cm
65 µs | 5cm
234 µs | 18 cm
247 µs | 19 cm
285 µs | 22 cm
PRP (µs) imaging depth (cm)

## Slide 22: How is PRF Altered When DOV is Adjusted?
PRF Definition: the number of ultrasound pulses the system transmits into the body each second.
Determined by the sound source.
PRF determined by the maximum imaging depth; adjustable by changing the DOV

## Slide 23
PRF
PRF is inversely related to DOV
Shallow imaging = higher PRF
Deep imaging = lower PRF
PRF ▼
PRF ▲

## Slide 24
For soft tissue:
PRF (Hz) = 77,000 cm/sec
imaging depth (cm)
In one sec. sound can travel into tissue and return from a depth of 77,000 cm. (one way distance)
= (154,000 / 2 =77,000)
Also means sound can travel:
To and from a depth of 77 cm 1,000 times in 1 sec
or
7.7 cm a total of 10,000 times in 1 sec
Speed of Sound
The speed of sound in soft tissue is 1,540 m/s or 154,000 cm/s.

## Slide 25
What is the PRF of a reflector when the DOV is set to 100 mm?
PRF (Hz) = 77,000 cm/sec
imaging depth (cm)
PRF (Hz) = 77,000 cm/sec
10 cm
PRF (Hz) = 7,700 Hz
100 mm = 10 cm. This formula specifies imaging
depth in units of cm.

## Slide 26
The primary interface of the intraventricular septal wall is located at a depth of 12 cm. What would the PRF be if the field of view is set to this depth?
PRF (Hz) = 77,000
imaging depth (cm)
PRF (Hz) = 77,000
12
PRF (Hz) = 6,416.7

## Slide 27
The sonographer alters his DOV to better visualize a structure. This structure is located at a depth of 130 mm, so the sonographer set the depth to 15 cm. What is the PRF?
PRF (Hz) = 77,000
imaging depth (cm)
PRF (Hz) = 77,000
15
PRF (Hz) = 5,133.3

## Slide 28
From our calculations what happens to the PRF as you increase depth?
100 mm | 7,000 Hz
120 mm | 6416.7 Hz
150 mm | 5133.3 Hz
160 mm | 4812.5 Hz
200 mm | 3850 Hz
DOV PRF

## Slide 29
Relationships
PRF is _________ related
to DOV

## Slide 30: Our Equations
Time of flight (ms) =depth cm x 13 (ms/cm)
Total distance traveled (cm)= depth to the reflector(cm) x 2
PRP (ms) = imaging depth cm x 13 (ms/cm)
PRF (Hz)= 77,000 (cm/s) / imaging depth (cm)