## Slide 1: Sonographers in the Clinical Setting
Chapter 23

## Slide 2: Major Principles of Medical Ethics
Respect for autonomy
  The patient has the capacity to act intentionally, with understanding, and with free will.
  Informed Consent
Nonmaleficence
  Avoid needless harm or injury to the patient.
Beneficence
  Actions of the health care providers should benefit the patient.
Justice
  Equal treatment regardless of age, gender, educational background, and other factors.

## Slide 3
Informed Consent
Patients are educated about the essentials of a medical procedure
Revocation of Consent
A patient may withdraw previously granted consent at any time

## Slide 4: Patient-Sonographer Interaction
Treat the patient respectfully
Identify the patient
Interpretation of the Exam
  Must be aware of normal & abnormal findings
  Refrain from providing a clinical interpretation to the patient
Patient Dignity
  Quality of being worthy, honored or esteemed
  Every patient deserves to be treated with dignity
  Perception of being in control & having self worth

## Slide 5
Standard Precautions
Set of guidelines to minimize the exposure and risk of healthcare workers when in contact with the patient
Personal Protective Equipment (PPE)
Occupational Safety and Health Administration (OSHA)
  All work should be classified based on potential exposure
  SOPs for all activities that have potential exposure
  Employers responsible for monitoring workers – documentation of procedures and evaluation of risk criteria

## Slide 6: Chapter 24: Bioeffects

## Slide 7: Bioeffects
The effects of ultrasound energy upon living tissues
In order to study the effects on living tissues, we must be able to measure the intensity and output of our ultrasound machines

## Slide 8: Bioeffects
Measuring the output of ultrasound machines can be done in several ways.
  Hydrophone-small needle with a crystal at its end.
  Placed in the ultrasound beam.
  Attaches to an oscilloscope and displays acoustic signals received by the crystal.
  Can quantitate amplitude, period, pulse duration, and pulse repetition period

## Slide 9: Radiation Force
  A sound beam creates a very small force on any object that it strikes.
    If the object is a balance or float, we can measure the SATA intensity.
    If a small suspended ball is used, we can measure the SPTA intensity.
  Essentially when the sound beam is absorbed or reflected, the target can act as a miniature scale.

## Slide 10: Acousto-Optics
Based on the interaction of two types of soundwaves and light waves.
Quantifies amplitude, period, pulse duration, and pulse repetition period.
A shadowing system called a SCHLIEREN, uses this principle to measure beam profiles

## Slide 11: Converting Sound Energy into Heat
Calorimeter – a transducer which turns acoustic energy into heat. When the total heat gain is measured along with the time that it took to obtain the heat, the total power of the US beam can be calculated.
Thermocouple – a small device embedded in an absorbing material. The ultrasound is absorbed, turned into heat, and the thermocouple measures the change in temperature. The US intensity at specific points in space are measured by a thermocouple.
Crystals – cholesteric liquid crystals or starch iodine blue, when struck by different ultrasound intensities, turns different colors. The color of the crystals give us insight into the shape and strength of a beam.

## Slide 12: Risk – Benefit Relationship
The first mandate regarding clinical ultrasound is that the benefits must outweigh the risks of the exam.
Extremely high ultrasound intensities can cause damage to biologic tissue.
Low-intensity ultrasound has no known bioeffects at this time.
Under controlled conditions, bioeffects can be beneficial.
  Therapeutic ultrasound (heats muscle tissues) or lithotripsy (shock waves to break up kidney stones)

## Slide 13: Dosimetry
  The science of identifying and measuring those characteristics of an US field which are especially relevant to its potential for producing bioeffects.

## Slide 14: In Vivo and In Vitro
Bioeffects studies are conducted in two areas
1) In Vivo – Within the living body
2) In Vitro – Outside the living body
In Vitro studies demonstrate that high intensity ultrasound can cause damage to biologic tissue and cellular death

## Slide 15: AIUM – In Vitro Bioeffects
Difficult to study in vivo because of attenuation
According to the official statement by the AIUM, No known causes of Bioeffects or tissue injury in diagnostic imaging at standard intensities
AIUM and FDA’s bioeffects intensity limit (SPTA)
    100 mW/cm2 unfocused
    1 w /cm2 or 1000 mW/cm2 focused

## Slide 16: Bioeffects
Focused vs. unfocused thermal effects
  Focused beams are less likely to cause temperature elevation in tissues
  Unfocused beams are more likely to cause temperature elevation
    This occurs because a narrow beam heats only a small region of tissue and the heat is rapidly transferred and dissipated by surrounding tissues that were not heated by the ultrasound beam.
Intensity limits: AIUM maximum intensity limit is lower for unfocused sound than for focused sound

## Slide 17: Bioeffects
Registry question note:
  If no information is provided in a question on whether a sound beam is focused or unfocused, chose the lower intensity limit (for unfocused beams) as the lower intensity limit is safe for focused and unfocused beams.

## Slide 18: Study Techniques
Two techniques used to study bioeffects:
Mechanistic Approach
Searches for a relationship between cause and effect
Empirical Approach
Searches for a relationship between exposure and response

## Slide 19: Study Techniques
Mechanistic approach
  Propose a specific physical mechanism that could produce bioeffects
  Theoretical analysis to estimate scope of bioeffects and various exposures
  Identify cause and effect relationship
Empirical Approach
  Acquire or review data from patients or animals
  Correlate exposure and effects
  Identify exposure-response relationship
STRONGEST CONCLUSIONS ARE MADE WHEN BOTH TECHNIQUES ARE IN AGREEMENT

## Slide 20: Mechanisms of Bioeffects : Thermal Mechanism
Proposes that bioeffects result from temperature elevation
  As sound propagates through the body energy is converted to heat
Thermal Index (TI) – a calculated number that is used to predict the maximum temperature increase in clinical conditions
Three reported forms of the thermal index are
A) TIS – Soft Tissue
B) TIB - Bone
C) TIC – Cranial Bone

## Slide 21: Thermal Mechanism - Empirical Findings
Serious tissue damage occurs from prolonged elevation of body temperature
Tissue heating is related to output characteristics of the transducer
A 2-4 degree rise in testicular temperature causes infertility
Maximal heating is related to the beams SPTA
Fetal tissues are less tolerant of the tissue heating

## Slide 22: Thermal Mechanism – Mechanistic Data
Theoretical models appear to correlate with experimental data even though:
  The ultrasound beam is quite complex
  Diagnostic equipment is diverse
  Tissue characteristics are different

## Slide 23: Mechanisms of Bioeffects: Nonthermal Mechanism - Cavitation
Cavitation – The interaction of ultrasound and microscopic stabilized gas bubbles in tissue
Two forms of Cavitation
1) Stable – Occurs at lower MI indices, The gaseous nuclei oscillate by do not burst
2) Transient – Occurs at higher MI levels, gaseous nuclei may burst

## Slide 24: Stable Cavitation
  Bubbles tend to oscillate when exposed to acoustic waves of small amplitude. Bubbles do not burst.
  Bubbles that are a few micrometers in diameter double in size.
  Effects: shear stresses and microstreaming in surrounding fluid

## Slide 25: Transient Cavitation
Bubbles expand and collapse violently.
Bubbles eventually burst!
Depends upon the pressure of the ultrasound pulse.
Threshold only 10% greater than pressure for stable cavitation
Effects are highly localized and violent
Enormous pressures
Colossal temperatures (thousands of degrees)
Under controlled conditions bioeffects are considered beneficial (therapeutic ultrasound)

## Slide 26: Mechanical Index
A calculated number related to the likelihood of harmful bioeffects from cavitation
MI is a simple number with no units
Related to two terms:
1) Peak negative pressure
2) Lower frequency

## Slide 27: Epidemiology and Statistics
We can study bioeffects with epidemiological studies
Epidemiological studies require large numbers of patients when the occurrence rate of the measured effect is small. (like diagnostic imaging)
Randomized clinical studies require large data sets on each patient to account for other factors which may contribute to the finding.
Using this method, diagnostic US has shown no adverse effects on fetal outcome or birth weight or any other measurement.

## Slide 28: Prospective & Randomized Studies
The best study is randomized and prospective
Limitations of epidemiological studies:
  often retrospective (looking at past information)
Ambiguities (justification for exam, number of exams)
Other risk factors (maternal age, nutrition, teratogens)
Statistical considerations:
  the smaller the effect, the harder it is to detect
  requires a large number of patients

## Slide 29: AIUM Conclusions
As of March 29, 1995
No confirmed harmful bioeffect from diagnostic ultrasound has ever been reported
It is possible that bioeffects may be reported in the future
The benefit to the patient outweighs the risks
It is appropriate to use diagnostic ultrasound prudently to provide benefit to the patient
It is never appropriate to use diagnostic ultrasound for entertainment

## Slide 30: ALARA
As
Low
As
Reasonably
Achievable

## Slide 31: Remember:
Benefits should always outweigh risks
Do not perform studies without reason
Minimize exposure time while still performing a complete exam
Always Use minimum output power and highest gain required to create an image