## Slide 1: ECHOCARDIOGRAPHY …From a Sonographer’s Perspective THE NOTEBOOK 8 Chapter V: Transesophageal Echocardiogram
Susan King DeWitt, BS, RDCS, RCS

## Slide 2
COPYRIGHT INFRINGEMENT IS A SERIOUS CRIME.
Please respect my U.S. Copyright & hard work—do not copy/distribute/edit.
Copyright © 1996, 2002, 2009, 2010, 2011, 2018, 2022. All rights reserved. Library of Congress Catalog Card Numbers: TX0006951179 and TX0008635753.
No part of this publication may be published, shared, edited, voiced over, reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise.
The information in this material is designed to provide education in the field of echocardiography and related topics. It was written, edited, and published by Susan King DeWitt, Author, LLC—a registered cardiac sonographer, not a physician, professional editor, or publishing company. This material does not guarantee a passing grade on the registry exam(s); however, it does discuss most of the test material. References provided do not constitute endorsement of any websites or other sources. Readers should be aware the information and websites listed may change.

## Slide 3
ECHO…THE NOTEBOOK 8 & THE WORKBOOK 8
are currently approved by the
Society of Diagnostic Medical Sonography (SDMS)
as a self-instructional activity for
31 CME CREDITS
Please refer to www.echonotebook.com for more details!

## Slide 4: V. TRANSESOPHAGEAL ECHO (TEE)
Discuss the fundamentals of a TEE, including the definition, patient education, advantages, disadvantages, indications, and contraindications.
Identify the role of the cardiac sonographer, physician, and nurse during the TEE.
Develop a basic knowledge of the TEE probe, windows, and views.
Classify the main types of TEE probes, including the multiplane, biplane, single plane, and pediatric probe.
Discuss some of the more modern TEE probes and procedures including the mini-multiplane probe, micro-multiplane probe, and transnasal echo.
OBJECTIVES
Upon completion of this section, the reader will be able to:

## Slide 5
TEE FUNDAMENTALS | 
DEFINITION TEE = transesophageal (via the esophagus) echocardiogram specialized probe  esophagus/stomach flexible & controllable shaft very small electronically steered (or mechanically rotated) ultrasound transducer mounted at distal tip of shaft 2D, M-mode & Doppler | THE TEAM cardiac sonographer nurse cardiologist or anesthesiologist
PATIENT EXPECTATIONS Education helps, but conscious sedation really helps! | 
POP QUIZ!
Explain the TEE as if speaking with a patient.

## Slide 6
start IV
prepare lab
patient education
conscious sedation
suction
collect & inspect equipment
operate machine
disinfect & store probe
inspect probe
spray anesthetic
insert probe
perform exam
interpret findings
monitor & document vitals
patient education
patient education
bubble study
POP QUIZ!
Name the team member!

## Slide 7
TEE FUNDAMENTALS | 
ADVANTAGES (over TTE) superior resolution less attenuation provides access in those who cannot be imaged via chest wall | DISADVANTAGES (compared to TTE) invasive procedure increased risk of complications increased discomfort & anxiety conscious sedation more expensive pediatric TEE  requires smaller probe, heavy sedation/anesthesia & well-trained staff additional supplies…
POP QUIZ!
Why does the TEE probe have superior
resolution over the TTE probe?

## Slide 8
PPE
conscious sedation & reversal agent
topical oropharyngeal anesthesia spray
disinfected TEE probe, sheath & bite block
crash cart, pulse ox, O2, nasal cannula, BP monitor & cuff
IV access & saline lock
tongue blade, lubricant, gauze squares & wash cloths
emesis basin, suction canister & tubing
bubble study supplies
towel/bag/other for used probe
post TEE protocol, designated area, disinfecting agent & storage
TEE worksheet, consent form & post care instructions
additional supplies

## Slide 9
TEE FUNDAMENTALS | 
CONTRAINDICATIONS pathologic condition of esophagus uncooperative/unwilling patient unstable respiratory status GI disorder/bleeding unstable cervical spine | INDICATIONS SOE, tumor, mass, myxoma, or thrombus IE/veg PHV dysfunction AO disease septal defect/shunt & bubble study VHD MI complications CMO HF technically limited TTE OR/cath guidance pediatric TEE
POP QUIZ!
Why is TEE superior to rule out a mass, particularly in the LA?

## Slide 10
According to the 2020 Guidelines for the Use of TEE to Assist with Surgical Decision-Making in the OR: A Surgery-Based Approach from the ASE in Collaboration with the Society of CV Anesthesiologists/Thoracic Surgeons, TEE should be used in adults (without contraindications) for all open heart & thoracic AO surgical procedures & considered in CABG surgeries to:
confirm/refine pre-op diagnosis,
detect new/unsuspected pathology,
adjust anesthetic & surgical plan,
assess results of surgical intervention.

## Slide 11
POP QUIZ!
Identify A & B.
A B

## Slide 12
TEE PROBES, WINDOWS & VIEWS | 
TYPES OF PROBES At first glance, all TEE probes appear similar! flexible shaft small transducer mounted on distal tip handle with deflection control wheels deflection brake | single plane probe biplane probe multiplane (aka omniplane) probe array rotation button array rotation gauge pediatric probes transnasal probe 3DE pulmonary vein evaluation
POP QUIZ!
What is the most popular TEE probe used today?

## Slide 13
POP QUIZ!
What makes the multiplane TEE probe so different from the older models?

## Slide 14
TEE PROBES, WINDOWS & VIEWS | 
TEE WINDOWS type of probe  quality & number of views multiplane probe most popular left lateral decubitus standard windows depth of probe from incisors determines window UE window ~ 20 - 25 cm deep ME window ~ 30 - 40 cm deep TG window via stomach ~ 40 - 50 cm deep deep transgastric DAO window is beyond TG rotate shaft to examine AO | MULTIPLANE VIEWS angulation & manipulation  multiple views adult ~ 20 standard views ASE recommends a series of 28 views for a comprehensive TEE in children & adults with CHD. LAX, SAX, 4C, 2C, inflow & outflow views
POP QUIZ!
Where is the TEE probe depth displayed?

## Slide 15
POP QUIZ! Match the name to the multiplane view.
DAO SAX ME AOV LAX ME AOV SAX ME 4C TG MID SAX UE AO ARCH LAX
A
C
B
D E F
Notes: ECHO…THE NOTEBOOK 6.5
CH 5, PG 133
ANSWER: (1 = B); (2 = C); (3 = E); (4 = D); (5 = A); (6 = F)