## Slide 1: ECHOCARDIOGRAPHY …From a Sonographer’s Perspective THE NOTEBOOK 8 Chapter VI: Stress Echocardiogram
Susan King DeWitt, BS, RDCS, RCS

## Slide 2
COPYRIGHT INFRINGEMENT IS A SERIOUS CRIME.
Please respect my U.S. Copyright & hard work—do not copy/distribute/edit.
Copyright © 1996, 2002, 2009, 2010, 2011, 2018, 2022. All rights reserved. Library of Congress Catalog Card Numbers: TX0006951179 and TX0008635753.
No part of this publication may be published, shared, edited, voiced over, reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise.
The information in this material is designed to provide education in the field of echocardiography and related topics. It was written, edited, and published by Susan King DeWitt, Author, LLC—a registered cardiac sonographer, not a physician, professional editor, or publishing company. This material does not guarantee a passing grade on the registry exam(s); however, it does discuss most of the test material. References provided do not constitute endorsement of any websites or other sources. Readers should be aware the information and websites listed may change.

## Slide 3
ECHO…THE NOTEBOOK 8 & THE WORKBOOK 8
are currently approved by the
Society of Diagnostic Medical Sonography (SDMS)
as a self-instructional activity for
31 CME CREDITS
Please refer to www.echonotebook.com for more details!

## Slide 4: VI. STRESS ECHO (SE)
Discuss the fundamentals of a SE, including the definition, purpose, team, advantages, indications, contraindications, and instrumentation.
Calculate the predicted MHR and THR.
Recognize the LV walls and their corresponding coronary artery.
List the criteria for a negative or positive SE.
Discuss the different SE protocols including the treadmill, supine bicycle, and dobutamine SE.
Recognize a few more SE protocols including perfusion imaging, coronary flow reserve, and 3D.
Gain knowledge of the current guidelines for the SE report.
OBJECTIVES
Upon completion of this section, the reader will be able to:

## Slide 5
SE FUNDAMENTALS
DEFINITION SE = stress test + echo detect IHD/CAD in those with angina or other symptoms flag risk for future cardiac events & assess prognosis
TYPES OF SE simultaneous assessment of electrical response (12 lead EKG) plus myocardial functional & hemodynamic response (echo) to stress (physiological or pharmacological stress test) ESE—TMSE or SBSE pharmacological SE—DSE or vasodilator
POP QUIZ!
Why is an ESE preferred
over pharmacological SE
& who determines the stressor?

## Slide 6
SE induces the hemodynamic effects of stress!
ischemia
WMA
valvular abnormality
myocardial supply & demand issue

## Slide 7
SE FUNDAMENTALS | 
THE TEAM specifically trained team patient education emergency prep stress tech nurse cardiac sonographer cardiologist | ADVANTAGES noninvasive, unless pharmacological SE &/or UEA no exposure relatively inexpensive quick & reliable  immediate feedback more sensitive & specific than standard stress test evaluate prior to stress  rule out contraindications abnormal EKG live, visual connection between symptoms & function
POP QUIZ!
What might be assessed during a SE to
connect symptoms to cardiac function?

## Slide 8
SE FUNDAMENTALS | 
INDICATIONS abnormal EKG athlete’s heart CAD/IHD CP unknown origin chest radiation exercise related arrhythmia exertional dyspnea evaluate prior to exercise program HF heart transplant LBBB | non-ischemic CMO predict prognosis pediatric SE/adult congenital patients at risk for IHD or to determine exercise tolerance pre-op clearance presence of risk factors previous non-diagnostic 12 lead EKG stress test PH RV function/TAPSE VHD
POP QUIZ!
What are the primary risk factors?

## Slide 9
ASE recommends that if a TTE has not been performed recently, a baseline resting TTE is necessary prior to stress. The presence of any contraindications must be noted & the SE postponed or canceled.

## Slide 10
SE FUNDAMENTALS | 
CONTRAINDICATIONS decreased (significantly) EF elevated cardiac enzymes known, severe CAD large AO aneurysm (unless pre-op) LVOTO mobile thrombus MI within past 48 hours myocarditis patient combative/uncooperative pericarditis | pregnant pulmonary embolus seizures significant EKG findings suboptimal images/technically difficult  consider UEA suspect recent MI that has not been fully evaluated syncope uncontrolled HTN unstable angina
POP QUIZ!
Define absolute vs relative contraindication.

## Slide 11
POP QUIZ!
What is the THR (90%)
of a 40-year-old?
SE FUNDAMENTALS
GOAL achieve THR desired THR = 85 - 90% of predicted MHR for at least 1 min predicted MHR = 220 - patient’s age THR = MHR x 0.90 (90% of their MHR) THR = MHR x 0.85 (85% of their MHR)
NORMAL CARDIAC RESPONSE (to stress/exercise) increase LV wall contractility decrease LV volume & size HR increases too!

## Slide 12
SE FUNDAMENTALS | 
DETECT IHD/CAD focus of chapter  detect IHD/CAD plaque  obstruction any location within any or all coronary arteries diseased coronary artery cannot properly feed heart muscle | WMA may not be obvious at rest, most appear during stress or immediate post stress If WMA appears at low stress? If WMA persists into recovery? If WMA presents toward base? If WMA presents toward apex?
POP QUIZ!
What might be detected by SE when CAD is present?

## Slide 13
WALL SEGMENTS |  |  |  |  | 
POP QUIZ! In general, what does each color represent?
Based on the Recommendations for Chamber Quantification by Echocardiography in Adults: An Update from the ASE and the European Association of Cardiovascular Imaging (J Am Soc Echocardiogr 2015; 28:1-39)

## Slide 14
CORONARY ARTERY DISTRIBUTION |  |  | 
(right dominant system) |  |  | 
Based on the Guidelines for Performance, Interpretation, & Application of SE in IHD: From the ASE (Jan 2020)

## Slide 15
SE FUNDAMENTALS | 
NEGATIVE SE normal global & regional wall motion at rest & at stress LV increases contractility LV decreases volume & size | POSITIVE SE segmental function & global function criteria for positive SE—fixed WMA or new/worsening WMA  ischemia resting WMA unchanged with stress  fixed WMA (prior MI) provoked regional WMA decrease in overall EF from rest to peak &/or immediate post increase in LVV & size from rest to peak &/or immediate post ischemia  delay onset of contraction & decrease velocity of contraction (tardokinesis vs other) false positive SE
POP QUIZ!
What does a fixed WMA usually represent?
POP QUIZ!
What is a normal LV response to stress?

## Slide 16
SE FINDINGS | + OR -
normal wall motion at rest  abnormal with stress | (1)
fixed WMA | (2)
normal LV wall motion at rest & at stress | (3)
increase in LVV & size from rest  peak/impost | (4)
new/worsening WMA indicative of ischemia | (5)
decrease in overall EF from rest  peak/impost | (6)
hypokinetic wall motion at rest  more hypokinetic or worse at peak/impost | (7)
POP QUIZ!
Fill in the blanks #1 - 7 as a positive or negative SE.

## Slide 17
SE FUNDAMENTALS | 
WMSI ideal WMSI = 1 16- or 17-segment model…What’s the difference? score of each segment is based on motion & systolic thickening WMSI = sum of all segments analyzed total # of segments analyzed normal or hyperkinesis = 1 hypokinesis = 2 severe hypokinesis or akinesis = 3 dyskinesis = 4 aneurysmal = 5 all or almost all segments must be visualized | According to the ASE, the UEA is indicated when 2+ contiguous segments &/or a coronary artery territory are not well visualized.
POP QUIZ!
How does the
UEA help?

## Slide 18
17 SEGMENT MODEL & CORONARY ARTERY DISTRIBUTION |  | 
CX = Left Circumflex Artery
LAD = Left Anterior Descending Artery
RCA = Right Coronary Artery
POP QUIZ!
If 17 segments are visualized & normal,
what is the WMSI?
Based on the Guidelines for Performance, Interpretation, & Application of SE in IHD: From the ASE (Jan 2020)

## Slide 19
POP QUIZ!
Identify the segments #1 - 17.

## Slide 20
SE INSTRUMENTATION
EQUIPMENT & ACQUISITION PPE, bed, EKG materials, EKG machine, ultrasound unit & TM/SB IV pump & UEA/meds for pharmacological SE integrated SE software permits digital acquisition & side-by-side display
IMPROVE SENSITIVITY tissue harmonic imaging UEA SBSE/DSE/pacing/vasodilator SE  ischemic threshold
According to the ASE, the UEA is indicated when 2+ contiguous segments &/or a coronary artery territory are not well visualized. In order to reduce cavity shadowing, the ASE suggests a very low dose bolus injection of the UEA followed by a slow saline flush.
POP QUIZ!
How does tissue harmonic
imaging improve sensitivity?
&
What is ischemic threshold?

## Slide 21
SE INSTRUMENTATION |  | 
CAPTURE SE type determines stage of image acquisition SE software  capture systolic/full beats off R wave REST, PEAK, IMPOST, FINAL | VIEWS LAX sax 4C 2C ? 3C ? unconventional views | QUAD SCREEN & CONTINUOUS LOOP sort through captured beats, select best  quad screen within each quadrant, each systolic/full beat broken down into 8 - 12 frames that repeat  continuous loop compare function at different HR review multiple cardiac cycles to improve accuracy digital preferred over videotape
IMAGE SELECTION & EDITING capture & select images carefully systolic vs diastolic frames |  | 
POP QUIZ!
Why is the quad screen necessary?

## Slide 22
TMSE
SBSE
DSE
TYPES OF SE

## Slide 23
SE PROTOCOLS | 
TMSE NPO 3 hours patient education—crucial! consent form gown enter patient data prep patient acquire REST EKG & BP enter patient data acquire REST images note patient position at rest practice breathing techniques cardiologist reviews REST data adjust TM to baseline (low & slow) patient straddles belt, then start TM | increase speed & grade every 3 mins (Bruce Protocol) or low level (Modified Bruce or Naughton Protocol) monitor/acquire EKG, BP & symptoms stop test: achieve THR for 1 min, significant symptoms, can’t go on, EKG changes, hypo/HTN, or cardiologist/patient stops test stop TM assist patient back into position & check EKG wire IMPOST images within 1 min document recovery select & compare REST to IMPOST generate preliminary report read with cardiologist review normal/ischemic response to TMSE (ECHO…THE NB7) QA
POP QUIZ!
Provide instructions for walking on the TM.

## Slide 24
SE PROTOCOLS | 
SBSE NPO 3 hours patient education consent form gown enter patient data prep patient acquire REST EKG & BP enter patient data acquire REST images practice breathing techniques cardiologist reviews REST data adjust bike to patient start pedaling increase resistance 25 - 50 watts/stage usually 2 or 3 min stages | maintain pace monitor/acquire echo, EKG, BP & symptoms remind patient to give a 1 min warning acquire PEAK images at peak stress or THR stop test: achieve THR for 1 min, significant symptoms, can’t go on, EKG changes, hypo/HTN, or cardiologist/patient stops exam stop pedaling acquire IMPOST images within 1 min acquire FINAL images after 1 min has passed document recovery select & compare REST to PEAK, IMPOST & FINAL generate preliminary report read with cardiologist review normal/ischemic response to SBSE (ECHO…THE NB7) QA
POP QUIZ!
What is the double product?

## Slide 25
SE PROTOCOLS | 
DSE NPO 3 hours patient education consent form gown enter patient data acquire REST EKG & BP nurse  IV access & preps pump enter patient data acquire REST images practice breathing exercises cardiologist reviews REST data start dobutamine infusion increase dose for 5 - 6 stages (3 min stages) | monitor/acquire echo, EKG, BP & symptoms acquire LOW DOSE images (stage I or II) if indicated, administer atropine stop test: reach THR or stage V/VI, significant symptoms, can’t go on, EKG changes, dizziness, hypo/HTN, or cardiologist/ patient stops exam acquire PEAK DOSE (stage V/VI, THR, or just before test terminated) acquire FINAL images post dobutamine document recovery select & compare REST to LOW DOSE, PEAK DOSE & FINAL generate preliminary report read with cardiologist review normal/ischemic response to DSE (ECHO…THE NB7) QA
POP QUIZ!
When is Atropine indicated?

## Slide 26
POP QUIZ!
Identify the SE quad screens A & B.
A
B

## Slide 27
MORE SE PROTOCOLS |  | 
PERFUSION IMAGING perfusion imaging with myocardial contrast echo DSE, ESE, or vasodilator perfusion abnormality occurs prior to WMA RTMCE using UEA | CORONARY FLOW RESERVE vasodilator SE high frequency TTE transducer assess coronary flow reserve via Doppler velocity of mid-distal LAD | 3DE 3DE during ESE or pharmacological SE detects CAD  rapid acquisition, excellent LV apex visualization & image all segments  lower frame rate, decreased spatial resolution & limited side-by-side comparison
POP QUIZ!
Can a perfusion defect occur in the absence of a WMA?

## Slide 28
SE REPORT
According to the 2020 ASE Guidelines, the following should be included… REST—regional wall motion assessment STRESS—regional wall motion assessment SE type/protocol ESE workload & adequacy Was THR achieved? Was stress inadequate/ischemia not detected? Graphic display of wall motion (REST & STRESS) Resting TTE findings Was SE indication exertional dyspnea? Overall interpretation—normal, ischemic, fixed WMA, or combo
POP QUIZ!
What should be acquired & reported if SE indication was exertional dyspnea?