## Slide 1: ECHOCARDIOGRAPHY …From a Sonographer’s Perspective THE NOTEBOOK 8 Chapter XX: Intro to 3D Echo & Real-time 3D/4DE
Susan King DeWitt, BS, RDCS, RCS

## Slide 2
COPYRIGHT INFRINGEMENT IS A SERIOUS CRIME.
Please respect my U.S. Copyright & hard work—do not copy/distribute/edit.
Copyright © 1996, 2002, 2009, 2010, 2011, 2018, 2022. All rights reserved. Library of Congress Catalog Card Numbers: TX0006951179 and TX0008635753.
No part of this publication may be published, shared, edited, voiced over, reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise.
The information in this material is designed to provide education in the field of echocardiography and related topics. It was written, edited, and published by Susan King DeWitt, Author, LLC—a registered cardiac sonographer, not a physician, professional editor, or publishing company. This material does not guarantee a passing grade on the registry exam(s); however, it does discuss most of the test material. References provided do not constitute endorsement of any websites or other sources. Readers should be aware the information and websites listed may change.

## Slide 3
ECHO…THE NOTEBOOK 8 & THE WORKBOOK 8
are currently approved by the
Society of Diagnostic Medical Sonography (SDMS)
as a self-instructional activity for
31 CME CREDITS
Please refer to www.echonotebook.com for more details!

## Slide 4: XX. Intro to 3D Echo (3DE) & Real-time 3D (RT3D/4DE)
Discuss a little bit of history, image quality, acquisition modes, and technical aspects of 3DE.
2. Gain knowledge of the RT3D/4DE transducer, acquisition modes, and technical factors.
3. List clinical applications of RT3D/4DE.
OBJECTIVES
Upon completion of this section, the reader will be able to:

## Slide 5
What is 3D, super cute,
& loves to chase bunnies?
poof!

## Slide 6
JackJack Attack!
(15-year-old Schnoodle)

## Slide 7
3DE
3DE vs 2D ECHO 3D  length, width & depth attempts at 3DE in the 60s first 3DE images acquired in the 70s ability to progress & develop 2D echo manage CHD 2D & 3DE—safe, noninvasive, assess function & anatomy 3DE shows improved accuracy & reproducibility 3DE systems becoming widely accessible
POP QUIZ!
With transthoracic imaging, what is the most common 3D application?

## Slide 8
3DE
METHOD series of 2D images  reconstruct 3D image 2D images acquired & processed offline not evaluated in real-time acquire serial 2D images freehand scanning mechanically driven transducer TEE probe TTE multiplane probe
POP QUIZ!
How are the images gated?

## Slide 9
POP QUIZ!
Label the 2D image & 3D image.
A B

## Slide 10
POP QUIZ!
Does LVV reconstruction
require fewer or more 2D images
than what a valve requires?
intrinsic quality & # of 2D images
ability to limit artifact
adequacy of EKG & respiratory gating
3DE quality

## Slide 11
3DE
TECHNICAL FACTORS similar to 2D echo avoid artifact optimal gain settings use gating to obtain volumetric data biggest challenge  respiratory difficulties &/or arrhythmias segmentation
POP QUIZ!
What is most artifact related to?

## Slide 12
3DE
PROTOCOL similar to 2D study ventricular function, valvular morphology & hemodynamic status inherently volumetric surface rendered vs volume rendered each plane can be viewed from two sides that represent opposite perspectives sagittal plane (LAX) viewed from left or right coronal plane (4C) viewed from above or below transverse plane (SAX) viewed from apex or base complete 3DE study vs selective, focused study acquisition & data processing to calculate LVEF via 3D volume set depend on ultrasound system
POP QUIZ!
What is the difference between surface & volume rendered 3DE?

## Slide 13
RT3D/4DE
HISTORY & DEFINITION Duke Univ developed first RT3D scanner in the 90s depicts real-time cardiac motion able to acquire volumetric data at adequate frame rates added 4th dimension RT3D & 4DE—interchangeable terms
POP QUIZ!
What is the 4th dimension?

## Slide 14
RT3D/4DE
FURTHER ADVANCES led to RT3D commercialization matrix-array transducer technology improved resolution smaller footprint improved side lobe suppression greater sensitivity & penetration harmonic capabilities display online 3D column-rendered images or 2 - 3 simultaneous orthogonal 2D imaging planes All-in-one 2D/RT3D transducer… a one-stop shop!
perks!!!

## Slide 15
POP QUIZ!
How does 4DE improve
LV quantification?
simplify with the push of a button
faster acquisition
simultaneously visualize multiple views
3DE pixels create depth
4C, zoom MV & TV
monitor device deployment
improved resolution
orientation while training
2D & 3DE
amber
blue-gray
observe both valves from SAX
observe valves from either side
pre/post ASD repair
observe from RA or LA
improve LV quantification
software tracks endocardium
sonographer doesn’t trace
More about
the all-in-one
2D/RT3D transducer…
a one-stop shop!

## Slide 16
RT3D/4DE
ACQUISITION MODES 3 acquisition modes image acquisition depends on structure being examined real-time or narrow zoom or magnified wide angle
ANALYSIS METHODS offline or online
POP QUIZ!
Compare narrow vs zoom vs wide angle acquisition.

## Slide 17
RT3D/4DE | 
CLINICAL APPLICATIONS evaluate cardiac chambers LV chamber & mass  LVV global function & regional wall motion remodeled ventricle post MI contrast if needed exercise & pharmacological SE RV chamber size, RVV & function LAV valve function valve shape, structure & flow surgical guide | CHD faster exam  less sedation surgical guide ventricular size & function via dimension, volume, mass & EF intraoperative apps contrast echo LVV surface identification volume LVEF
POP QUIZ!
What makes RT3D super useful
in the assessment of CHD?